## Slide 1
MARINE HVAC
DIGITAL TWIN
Activity-Based Learning & Incident Simulation
PRESENTED BY:
Cyril Dheeran (2303608023)
Mohammed Dhafiq (2303608039)
M Athul Dev (2303608037)
Afsal Rahman J (2303608008)
LAUNCH LIVE APPLICATION ↗

## Slide 2
SYS.MONITOR // ACTIVE
MODULE_01A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 1: REGINA SEAWAYS
INCIDENT OVERVIEW & VESSEL PROFILE
Vessel Classification: DFDS Regina Seaways (Commercial Ro-Ro Passenger Ferry).
Incident Environment: Underway in the Baltic Sea, en route to Klaipeda, Lithuania (October 2018).
Initial Trigger: Excessive block vibration detected, culminating in a catastrophic mechanical breakdown of the starboard main engine.
Primary Hazard: Internal engine components structurally breached the crankcase, instantly igniting an uncontained engine room fire.

## Slide 3
SYS.MONITOR // ACTIVE
MODULE_01B // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 1: REGINA SEAWAYS
TECHNICAL HVAC FLAW & CASCADING FAILURE
Structural Design Flaw: Port and starboard engine compartments shared interconnected ambient ventilation ducting.
Missing Safeties: The shared duct lacked automatic, heat-triggered fire isolation dampers.
Cross-Contamination: The running port engine created negative pressure, pulling toxic smoke from the starboard fire directly into its own air intakes.
Ultimate Consequence: The port engine aspirated particulate matter, choked, and stalled. The vessel suffered a total blackout and loss of propulsion.

## Slide 4
SYS.MONITOR // ACTIVE
MODULE_01C // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
REAL-WORLD AFTERMATH: REGINA SEAWAYS
ACTUAL INCIDENT PHOTO
INSERT ACTUAL INCIDENT PHOTO HERE
(Real-world picture of the vessel or aftermath)

## Slide 5
SYS.MONITOR // ACTIVE
MODULE_01D // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SIMULATION: REGINA SEAWAYS
CRITICAL DECISION REQUIRED
INSERT DIGITAL TWIN SCREENSHOT HERE
(Action: Manually Close Isolation Dampers)

## Slide 6
SYS.MONITOR // ACTIVE
MODULE_02A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 2: F/V KALTAN
INCIDENT OVERVIEW & VESSEL PROFILE
Vessel Classification: Commercial Fishing Trawler.
Incident Environment: Docked for out-of-service repairs at Gamcheon Port, Busan, South Korea (September 15, 2026).
Initial Trigger: A compromised mechanical seal failed entirely on the main Freon refrigeration compressor during routine maintenance.
Primary Hazard: High-pressure Freon coolant evacuated from the system rapidly, triggering pressure drop alarms on the bridge.

## Slide 7
SYS.MONITOR // ACTIVE
MODULE_02B // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 2: F/V KALTAN
GAS PHYSICS & CONFINED SPACE HAZARD
Fluid Dynamics of Freon: Refrigerant gases like Freon are significantly heavier than ambient air.
The Invisible Trap: Rather than dissipating, the toxic gas behaved like a fluid, flowing down deck stairs and displacing lighter oxygen.
Accumulation Zone: The gas pooled in the lowest point of the vessel—the unventilated lower fish hold.
Fatal Human Error: Crewmen breached protocol by entering the confined space to inspect the leak without SCBA gear, resulting in rapid asphyxiation.

## Slide 8
SYS.MONITOR // ACTIVE
MODULE_02C // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
REAL-WORLD AFTERMATH: F/V KALTAN
ACTUAL INCIDENT PHOTO
INSERT ACTUAL INCIDENT PHOTO HERE
(Real-world picture of the vessel or aftermath)

## Slide 9
SYS.MONITOR // ACTIVE
MODULE_02D // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SIMULATION: F/V KALTAN
CRITICAL DECISION REQUIRED
INSERT DIGITAL TWIN SCREENSHOT HERE
(Action: Require SCBA Gear Before Entry)

## Slide 10
SYS.MONITOR // ACTIVE
MODULE_03A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 3: INS RANVIR
INCIDENT OVERVIEW & VESSEL PROFILE
Vessel Classification: Rajput-class guided-missile destroyer, Indian Navy.
Incident Environment: Naval Dockyard, Mumbai, India (January 2022).
Operation: Shore contractors boarded the vessel for routine maintenance and topping up of the forward AC plant's R-22 refrigerant.
Primary Hazard: A massive supply chain error. Contractors unknowingly attached a cylinder containing R-152a—a highly flammable hydrocarbon gas.

## Slide 11
SYS.MONITOR // ACTIVE
MODULE_03B // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 3: INS RANVIR
THERMOBARIC EXPLOSION MECHANISM
System Mismatch: Pumping R-152a into an R-22 system caused immediate pressure imbalances, blowing the compressor casing seal.
Gas Accumulation: The forward machinery room rapidly filled with the unventilated, combustible hydrocarbon vapor.
Ignition Source: The pooling gas reached a nearby electrical panel just as an automatic contactor relay tripped, generating a high-voltage spark.
Ultimate Consequence: The spark ignited the hydrocarbon gas, causing a devastating thermobaric explosion and hull breach.

## Slide 12
SYS.MONITOR // ACTIVE
MODULE_03C // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
REAL-WORLD AFTERMATH: INS RANVIR
ACTUAL INCIDENT PHOTO
INSERT ACTUAL INCIDENT PHOTO HERE
(Real-world picture of the vessel or aftermath)

## Slide 13
SYS.MONITOR // ACTIVE
MODULE_03D // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SIMULATION: INS RANVIR
CRITICAL DECISION REQUIRED
INSERT DIGITAL TWIN SCREENSHOT HERE
(Action: Emergency Halt - Flammable R-152a Detected)

## Slide 14
SYS.MONITOR // ACTIVE
MODULE_04A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 4: AL-SALAM BOCCACCIO 98
INCIDENT OVERVIEW & VESSEL PROFILE
Vessel Classification: Heavy Egyptian Ro-Ro (Roll-on/Roll-off) Passenger Ferry.
Incident Environment: Open waters in the Red Sea, sailing from Duba to Safaga (February 2006).
Initial Trigger: A localized fire sparked in the lower vehicle deck, suspected to have originated in a parked cargo vehicle.
Primary Hazard: Smoke alarms triggered on the bridge, and crew members began firefighting operations using high-volume seawater hoses.

## Slide 15
SYS.MONITOR // ACTIVE
MODULE_04B // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
CASE STUDY 4: AL-SALAM BOCCACCIO 98
VENTILATION ERROR & FREE SURFACE EFFECT
HVAC Operational Error: Crew failed to shut down the massive forced-draft supply and exhaust ventilation fans on the vehicle deck.
Fire Dynamics: The continuous flow of fresh oxygen acted as a massive bellows, expanding the localized fire uncontrollably.
Drainage Failure: To fight the massive fire, tons of seawater were pumped in, but blocked deck scuppers trapped the water onboard.
Ultimate Consequence: The trapped water sloshed across the deck (Free Surface Effect), destabilizing the center of gravity and capsizing the ferry.

## Slide 16
SYS.MONITOR // ACTIVE
MODULE_04C // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
REAL-WORLD AFTERMATH: AL-SALAM BOCCACCIO 98
ACTUAL INCIDENT PHOTO
INSERT ACTUAL INCIDENT PHOTO HERE
(Real-world picture of the vessel or aftermath)

## Slide 17
SYS.MONITOR // ACTIVE
MODULE_04D // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SIMULATION: AL-SALAM BOCCACCIO 98
CRITICAL DECISION REQUIRED
INSERT DIGITAL TWIN SCREENSHOT HERE
(Action: Emergency Stop Ventilation Fans)

## Slide 18
SYS.MONITOR // ACTIVE
MODULE_05A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
DIGITAL TWIN ARCHITECTURE
HOW THE LIVE SIMULATOR WORKS
1. USER INPUTS
React State Variables
(Ambient Temp, Sea Temp, Valve %, Compressor Load)
2. THERMODYNAMIC ENGINE
Calculates real-time Condenser Pressures, Cooling Effects, and Humidity Deltas based on physical limits.
3. UI RENDER
Updates UI SVGs,
Triggers Logic Alarms
// Live Logic Snippet
const condenserPress = Math.max(4.0, 10 + ((seaTemp - 20) * 0.8) + (activeLoad * 0.05));
const coolingEffect = isTripped ? 0 : (coolerValve / 100) * maxCoolingDelta;
const cabinHumidity = 40 + (humidifierValve / 100 * 40) - (coolerValve / 100 * 15);

## Slide 19
SYS.MONITOR // ACTIVE
MODULE_06A // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SYSTEM SIMULATOR: REFRIGERATION PLANT
PROVISION REFRIGERATION MONITORING
INSERT SCREENSHOT
(Simulator Tab: Refrigeration Plant showing Meat/Veg Rooms)

## Slide 20
SYS.MONITOR // ACTIVE
MODULE_06B // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SYSTEM SIMULATOR: AIR HANDLING UNIT
AC AIR HANDLING UNIT (AHU) CONTROLS
INSERT SCREENSHOT
(Simulator Tab: AHU View showing Cabin Temp and Humidity)

## Slide 21
SYS.MONITOR // ACTIVE
MODULE_06C // LIVE
MARINE HVAC DIGITAL TWIN v1.0
HVAC.TWIN
SYSTEM SCHEMATIC & PIPING DIAGRAM
HVAC LINE DIAGRAM
INSERT SCHEMATIC IMAGE
(Paste an actual line diagram or piping schematic here)